## Slide 1: Design for X
Professor Richard Lee Storch
IND E 494
Design in the Manufacturing Firm

## Slide 2: Reference
Ulrich, K. & Eppinger, S. (2000). Product
Design and Development. Boston, MA: Irwin McGraw-Hill.

## Slide 3: Design for X Topics
Design for Manufacturing
Design for Production
Design for Assembly
Design for Recycling/Disposal
Design for Life Cycle
Prototyping

## Slide 4: Gathering DFM Information
Sketches, drawings, product specifications, and design alternatives.
A detailed understanding of production and assembly processes
Estimates of manufacturing costs, production volumes, and ramp-up timing.

## Slide 5: DFM Method

## Slide 6: DFM Method
Estimate the manufacturing costs.
Reduce the costs of components.
Reduce the costs of assembly.
Reduce the costs of supporting production.
Consider the impact of DFM decisions on other factors.

## Slide 7: Estimate the Manufacturing Costs

## Slide 8: Manufacturing Costs Defined
Sum of all the expenditures for the inputs of the system (i.e. purchased components, energy, raw materials, etc.) and for disposal of the wastes produced by the system

## Slide 9: Elements of the Manufacturing Cost of a Product

## Slide 10: Manufacturing Cost of a Product
Component Costs (parts of the product)
  Parts purchased from supplier
  Custom parts made in the manufacturer’s own plant or by suppliers according to the manufacturer’s design specifications
Assembly Costs (labor, equipment, & tooling)
Overhead Costs (all other costs)
  Support Costs (material handling, quality assurance, purchasing, shipping, receiving, facilities, etc.)
  Indirect Allocations (not directly linked to a particular product but must be paid for to be in business)

## Slide 11: Fixed Costs vs. Variable Costs
Fixed Costs – incurred in a predetermined amount, regardless of number of units produced (i.e. setting up the factory work area or cost of an injection mold)
Variable Costs – incurred in direct proportion to the number of units produced (i.e. cost of raw materials)

## Slide 12: Reduce the Cost of Components
Understand the Process Constraints and Cost Drivers
Redesign Components to Eliminate Processing Steps
Choose the Appropriate Economic Scale for the Part Process
Standardize Components and Processes
Adhere to “Black Box” Component Procurement

## Slide 13: Understand the Process Constraints and Cost Drivers
Redesign costly parts with the same performance while avoiding high manufacturing costs.
Work closely with design engineers—raise awareness of difficult operations and high costs.

## Slide 14: Redesign Components to Eliminate Processing Steps
Reduce the number of steps of the production process
  Will usually result in reduce costs
Eliminate unnecessary steps.
Use substitution steps, where applicable.
Analysis Tool – Process Flow Chart and Value Stream Mapping

## Slide 15: Choose the Appropriate Economic Scale for the Part Process
Economies of Scale – As production volume increases, manufacturing costs usually decrease.
Fixed costs divided among more units.
Variable costs are lower since the firm can use more efficient processes and equipment.

## Slide 16: Standardize Components and Processes
Economies of Scale – The unit cost of a component decreases as the production volume increases.
Standard Components—common to more than one product
Analysis tools – group technology and mass customization

## Slide 17: Adhere to “Black Box” Component Procurement
Black box—only give a description of what the component has to do, not how to achieve it
Successful black box design requires clear definitions of the functions, interfaces, and interactions of each component.

## Slide 18: Reduce the Costs of Assembly
Design for Assembly (DFA) index
Integrated Parts (Advantages and Disadvantages)
Maximize Ease of Assembly
Consider Customer Assembly

## Slide 19: DFA Systems
Boothroyd Dewhurst DFM & A
Munro & Assoc. (Design Prophet/Profit)
Others

## Slide 20: Design for Assembly Index

## Slide 21: Determining the Theoretical Minimum Number of Parts
Does the part need to move relative to the rest of the assembly?
Must the part be made of a different material from the rest of the assembly for fundamental physical reasons?
Does the part have to be separated from the assembly for assembly access, replacement, or repair?

## Slide 22: Advantages of Integrated Parts
Do not have to be assembled
Often less expensive to fabricate rather than the sum of each individual part
Allows critical geometric features to be controlled by the part fabrication process versus a similar assembly process

## Slide 23: Disadvantages of Integrated Parts
Conflict with other sound approaches to minimize costs
Not always a wise strategy

## Slide 24: Minimize Ease of Assembly
Part is inserted from the top of the assembly
Part is self-aligning
Part does not need to be oriented
Part requires only one hand for assembly
Part requires no tools
Part is assembled in a single, linear motion
Part is secured immediately upon insertion

## Slide 25: Consider Customer Assembly
Customers will tolerate some assembly
Design product so that customers can easily and assemble correctly
Customers will likely ignore directions

## Slide 26: Reduce the Costs of Supporting Production
Minimize Systemic Complexity (inputs, outputs, and transforming processes)
  Use smart design decisions
Error Proofing (Poka Yoke)
  Anticipate possible failure modes
  Take appropriate corrective actions in the early stages
  Use color coding to easily identify similar looking, but different parts

## Slide 27: Consider the Impact of DFM Decisions on Other Factors
Development Time
Development Cost
Product Quality
External Factors
  Component reuse
  Life cycle costs

## Slide 28: Design for Production
Design Organization
Timing of Production
Material Identification
Specific Design Details (outputs)

## Slide 29: Production Input
At various design stages
  Concept
    Production Input
  Functional
    None
  Transition
    Tactics
  Work Instruction
    Production Preparation

## Slide 30: New Idea: Provide Production Inputs
In proper level of detail at proper stage
In proper form
Just-in-time

## Slide 31: Problems with Old Approach
Work is carried out from beginning to end at each stage
Too slow
Needs continuous recycling

## Slide 32: Design for Production General Principles
Use Common Sense
Plan and Define
Consider Available Facilities
Consider Available Tools
Consider Available Worker Skills
Employ Simplicity
Standardize

## Slide 33: Design for Production Guidelines
Minimize Total Number of Parts
Develop a Modular Design
Minimize Part Variations
Design Parts to be Multifunctional
Design Parts for Multiuse
Design Parts for Ease of Fabrication
Avoid Separate Fasteners

## Slide 34: Design for Production Guidelines (Cont.)
Minimize Assembly Direction (Top Down Direction Preferred)
Maximize Compliance in Assembly
Minimize Handling in Assembly
Minimize complexity of Design
Maximize common Jigs and Fixtures
Optimize Work Position
Ease Access

## Slide 35: Types of Prototypes
Two dimensions
  Physical vs. Analytical
  Comprehensive vs. Focused

## Slide 36: Physical vs. Analytical
Physical
  Tangible artifacts created to approximate the product
  Used for testing and experimentation
Analytical
  Represents the product in a nontangible, usually mathematical manner
  Product is analyzed, not built

## Slide 37: Comprehensive vs. Focused
Comprehensive
  Implement all (or most) of the attributes of the product
  Full-scale
  Fully operational version of the product
Focused
  Implement a few of the attributes of the product
  Use two or more focused prototypes together to investigate the overall performance of a product

## Slide 38: Prototype Uses
Learning
  Will it work?
  How well does it meet the customer needs?
Communication
  Within the company
  With customers, vendors, and suppliers
Integration
  Subsystems and components work together
Milestones
  Product achieved a desired level of functionality

## Slide 39: Principles of Prototyping
Analytical Prototypes are generally more flexible than Physical Prototypes
Physical Prototypes are required to detect unanticipated phenomena
A Prototype may reduce the risk of costly iterations
A Prototype may expedite other development steps
A Prototype may restructure task dependencies

## Slide 40: Use of comprehensive prototypes

## Slide 41: Prototyping Technologies
3D Computer Modeling
  Easily visualize the 3D form of the design
  Automatically compute physical properties
  Other more focused descriptions can be created based on one design
  Detect geometric interference among parts

## Slide 42: Prototype Technologies Cont.
Free-Form Fabrication (or Rapid Prototyping)
  3D printers that create physical objects directly from 3D computer models
  Less expensive
  Reduce product development time, improve resulting product

## Slide 43: Planning for Prototypes
Define the purpose of the prototype
Establish the level of approximation of the prototype
Outline an experimental plan
Create a schedule for procurement, construction, and test

## Slide 44: Define the Purpose
List specific learning and communication goals
List any integration needs
Determine if the prototype is intended to be one of the major milestones of the overall product development project

## Slide 45: Establish the Level of Approximation
Determine physical or analytical prototype
Choose the simplest prototype that will serve the purpose established in step 1.
Consider existing prototypes or a another prototype being built that can be borrowed

## Slide 46: Outline an Experimental Plan
Use prototype for experimentation
Extract the maximum value from the prototyping activity.
Identify the variables of the experiment, test protocol, plan for analyzing the resulting data

## Slide 47: Create a Schedule for Procurement, Construction, and Test
Determine when parts are ready to be assembled
Determine the date when prototype will be first tested
Determine expectations for completed testing and final results

## Slide 48: Milestone Prototypes
Alpha Prototypes – assess whether the product works as intended
Beta Prototypes – assess reliability and to identify any bugs in the product
Preproduction Prototypes – first products produced by the entire production process